DATA ANALYSIS FOR VIBRATION DETECTION ALGORITHM

Starting with a known scenario: CHAINSAW CUTTING AT 70CM FROM THE SENSOR DURING 5MIN.
So that we can TEST:

Ground Truth Validation: Confirming whether our simulated classifier correctly maps to real-world vibration patterns.

Baseline Calibration: Real data will always contain environmental noise, slight hardware delays, and sensor quirks — testing known conditions lets us fine-tune energy thresholds and frequency band ranges.

Event Shape Matching: It should help validate that our previous assumptions (e.g., machete = sharp energy in D3–D4) hold true in real wood, not just simulated signals.

Comparative Analysis: Once one known event works (say, chainsaw), we can use its band pattern as a benchmark to distinguish others (wind, machete, etc.).

WORKFLOW CHOSEN:
Starting with: CHAINSAW CUTTING AT 70CM FROM THE SENSOR DURING 5MIN.
Picked 5 .csv files at random from that batch to test with the wavelet classifier.
Visualize + Classify:
- Plot the signal
- Perform DWT
- Compute energy ratios for D1–D5
- Apply the classifier logic
- known expected activity = CHAINSAW
Compare Output with known expected activity.

THINGS TO CHANGE IN DATA COLLECTION:
-sensor is aligned in the x axis and y , z are almost superimposed signals. Maybe try installing the sensor horizontally
-Collect more data but using machete as well.
-Collect a new batch of data using the newly added variables like temp and total magnitude.